## Slide 1: DRAM Caching for a FAM-aware Key-value store
Sekwon Lee
sekwonl@hpe.com
20 September 2017

## Slide 2: Fabric-Attached Memory (FAM) aware Key-Value Store (KVS)
Leverage large pool of FAM to persistently store data
Non-volatile memory (NVM) has longer load/store access latency than DRAM
To reduce the number of accesses to FAM, DRAM can be used for caching key-value pair from FAM
FAM
CPU
DRAM
I/O
CPU
DRAM
I/O
…
CPU
DRAM
I/O
1
2
N
Memory Interconnect
KVS

## Slide 3: What should we store in DRAM cache?
Overheads when cache miss occur
  1. traversal for FAM index structures
  2. data copy overhead from FAM
If we assume that the nodes are never deleted once allocated
  For deterministic index structure like radix tree, the address of key nodes is not changed
  With pointer value, we can easily access FAM area
  Short-cut pointer can be usefully cached for skipping index traversal
ROOT
V
r
roman
V
u
romanus
V
romane
V
e
1
2
romane 1
romanus 2
Short-cut

## Slide 4: Single node
FAM
CPU
DRAM
I/O
Memory Interconnect
KVS

## Slide 5: DRAM caching for a FAM-aware Key-value store
Three approaches
  1. Full cache <key, value, short-cut>
    Caching full key-value pair with short-cut pointers
    Read hit: return value from DRAM cache
    Update hit: bypass index traversal
  2. Short-cut cache <key, short-cut>
    Caching only key and short-cut pointers
    Hit: access to key node with short-cut pointer and directly return value from FAM
    Cache hit rate per cache size can be increased
    Ease to decide the upper bound of cache size depending on the number of keys
  3. Hybrid cache
    Hot data is stored with full key-value pair
    Cold data is stored only with short-cut
<K, V, short-cut>
<K, V, short-cut>
<K, V, short-cut>
K short-cut
K short-cut
K short-cut
K short-cut
K short-cut
<K, V, short-cut>
<K, V, short-cut>
<K, V, short-cut>
K short-cut
K short-cut
K short-cut
K short-cut
K short-cut
Eviction
Hot
Cold
Hit

## Slide 6: Implementation platform
Memcached
  Key-value cache that is broadly used for DRAM cache (Facebook, Twitter)
  Memcached variant is attached at the front end of FAM-aware KVS
    Provide server and local API
    Support storing short-cut pointer
Key Value Store
Radix Tree
Hash Table
Cache API (Memcached)
Hash table
LRU list
Slab allocator
Local APP or Server
Put
Get

## Slide 7: Experimental environment
Intel(R) Xeon(R) CPU E5-2687W v3 @ 3.10GHz X 2 (CPU cache size 25 MB)
FAM is emulated with 64GB of 128GB DRAM
  NVM latency (1000ns) is configured with Quartz
    Quartz: A DRAM-based performance emulator for NVM (https://github.com/HewlettPackard/quartz)
DRAM cache size is 4MB and the size of whole dataset is 1GB
  4MB cache size can cover about 4,000 key-value pair
Benchmark
  YCSB (Yahoo! Cloud Serving Benchmark)
    Balanced: 50% reads, 50% updates
    Read-Heavy: 95% reads, 5% updates
  Request pattern (one million requests, two worker threads)
    Uniform
      High skew: transactions access to 0.5% of keys (5,000 keys)
      Low skew: transactions access to 5% of keys (50,000 keys)
    Zipfian
      Transactions frequently access to the same keys

## Slide 8: Experimental environment
Comparison group
Label | Cache policy |  | 
 | key | value | Short-cut
KVS | X | X | X
MC (Memcached) | O | O | X
Full | O | O | O
Short | O | X | O
Hybrid | O | O | O

## Slide 9: Balanced (50% read / 50% update)
When using cache with KVS, there is additional cache update overhead with KVS update
Chart: High skew
kvs | 94.9694
MC | 100.03
full | 120.347
short | 168.8983
hybrid | 140.2567
Chart: Low skew
kvs | 83.5825
MC | 69.9683
full | 71.5539
short | 82.2734
hybrid | 74.9409
Chart: Zipfian
kvs | 105.2827
MC | 93.0324
full | 114.8453
short | 112.557
hybrid | 115.4143

## Slide 10: Balanced (50% read / 50% update)
When using cache with KVS, there is additional cache update overhead with KVS update
Cache policies with short-cut pointer show performance advantage from cache even with many update operations
Chart: High skew
kvs | 94.9694
MC | 100.03
full | 120.347
short | 168.8983
hybrid | 140.2567
Chart: Low skew
kvs | 83.5825
MC | 69.9683
full | 71.5539
short | 82.2734
hybrid | 74.9409
Chart: Zipfian
kvs | 105.2827
MC | 93.0324
full | 114.8453
short | 112.557
hybrid | 115.4143

## Slide 11: Read-Heavy (95% read / 5% update)
Chart: High skew
kvs | 115.9857
MC | 198.2513
full | 205.0157
short | 239.6843
hybrid | 267.4667
Chart: Low skew
kvs | 74.2574
MC | 69.8064
full | 69.9946
short | 79.3382
hybrid | 73.4473
Chart: Zipfian
kvs | 127.1687
MC | 254.3437
full | 272.7157
short | 178.731
hybrid | 271.2597
Except for the case where hit rate is low (Low skew), performance advantage from cache is clear in read-heavy workload

## Slide 12: Read-Heavy (95% read / 5% update)
Chart: High skew
kvs | 115.9857
MC | 198.2513
full | 205.0157
short | 239.6843
hybrid | 267.4667
Chart: Low skew
kvs | 74.2574
MC | 69.8064
full | 69.9946
short | 79.3382
hybrid | 73.4473
Chart: Zipfian
kvs | 127.1687
MC | 254.3437
full | 272.7157
short | 178.731
hybrid | 271.2597
Except for the case where hit rate is low (Low skew), performance advantage from cache is clear in read-heavy workload
Uniform skew: short-cut and hybrid approaches show better performance than full approach
  In uniform workload, short-cut and hybrid can cover more keys

## Slide 13: Read-Heavy (95% read / 5% update)
Chart: High skew
kvs | 115.9857
MC | 198.2513
full | 205.0157
short | 239.6843
hybrid | 267.4667
Chart: Low skew
kvs | 74.2574
MC | 69.8064
full | 69.9946
short | 79.3382
hybrid | 73.4473
Chart: Zipfian
kvs | 127.1687
MC | 254.3437
full | 272.7157
short | 178.731
hybrid | 271.2597
Except for the case that hit rate is low (Low skew), performance advantage from cache is clear in read-heavy workload
Uniform skew: short-cut and hybrid approaches show better performance than full approach
  In uniform pattern, short-cut and hybrid can cover more keys
Zipfian: full and hybrid approaches show better performance than short-cut
  In zipfian pattern, short-cut approach have to access FAM for copying data while full and hybrid can directly return value from cache

## Slide 14: Multi-nodes
FAM
CPU
DRAM
I/O
CPU
DRAM
I/O
…
CPU
DRAM
I/O
1
2
N
Memory Interconnect
KVS

## Slide 15: KVS cache consistency
Stale data can remain after KVS data is updated
CPU
DRAM
I/O
CPU
DRAM
I/O
…
CPU
DRAM
I/O
1
2
N
Memory Interconnect
FAM
v2
v1
v2
v2
Inconsistent

## Slide 16: Solutions for overcoming KVS cache inconsistency
Two approaches
  No sharing: partitioned
    Pros: removes coordination overheads
    Cons: load imbalance for skewed workloads
  Sharing: shared data
    Pros: load balance
    Cons: high coordination overheads
  Which approach will be better
Caching & No sharing | Caching & Sharing
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network

## Slide 17: Version number-based approach for sharing
Version number embedded in value pointer enables check whether cache entry is up-to-date or not
Value pointer that consists of globally-visible address and version number (16 bytes) can be atomically updated
Version number is incremented when value is updated or deleted
DRAM cache entry contains
  <key, value, short-cut pointer, pointer to value in FAM>
Short-cut pointer can reduce FAM access overhead
  Version-based approach may have to access FAM multiple times on cache miss.

## Slide 18: Local DRAM cache policy
Partitioned |  | Version-based | 
Hit | Cached data can be directly returned | Hit | Access to FAM for checking the version of data
Miss | Access to FAM and add new data to cache | Miss | Access to FAM and add new data to cache
Cons | Load imbalance | Cons | Frequent FAM access
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network

## Slide 19: Read-Heavy (95% read / 5% update)
Chart: Throughput (KTPS)
| High skew | Low skew | Zipfian
kvs | 115.9857 | 74.2574 | 127.1687
hybrid-partitioned | 267.4667 | 73.4473 | 271.2597
hybrid-versioned | 222.7137 | 74.1055 | 206.4777
short-versioned | 239.6843 | 79.3382 | 178.731
Version based hybrid approach show 20~30% worse performance than partitioned mode
  This performance difference is caused by data copy overhead from FAM in versioned approach
20%
30%
Single node performance

## Slide 20: Read-Heavy (95% read / 5% update)
Chart: Throughput (KTPS)
| High skew | Low skew | Zipfian
kvs | 115.9857 | 74.2574 | 127.1687
hybrid-partitioned | 267.4667 | 73.4473 | 271.2597
hybrid-versioned | 222.7137 | 74.1055 | 206.4777
short-versioned | 239.6843 | 79.3382 | 178.731
Version based hybrid approach show 20~30% worse performance than partitioned mode
  This performance difference is caused by data copy overhead from FAM in versioned approach
Version based short-cut approach show 11% worse performance but, 7% better performance in low skew
11%
7%
Single node performance

## Slide 21: Balanced (50% read / 50% update)
Chart: Throughput (KTPS)
| High skew | Low skew | Zipfian
kvs | 94.9694 | 83.5825 | 105.2827
hybrid-partitioned | 140.2567 | 74.9409 | 115.4143
hybrid-versioned | 137.447 | 74.9625 | 110.255
short-versioned | 168.8983 | 82.2734 | 112.557
Lower performance difference than read-heavy workload between hybrid approaches
  YCSB’s update operation changes existing 1KB data block with 100bytes
  Data copy overhead is lower than read-heavy workload (1KB copy vs 100bytes copy)
5%
5%
Single node performance

## Slide 22: Balanced (50% read / 50% update)
Chart: Throughput (KTPS)
| High skew | Low skew | Zipfian
kvs | 94.9694 | 83.5825 | 105.2827
hybrid-partitioned | 140.2567 | 74.9409 | 115.4143
hybrid-versioned | 137.447 | 74.9625 | 110.255
short-versioned | 168.8983 | 82.2734 | 112.557
Lower performance difference than read-heavy workload between hybrid approaches
  YCSB’s update operation changes existing 1KB data block with 100bytes
  Data copy overhead is lower than read-heavy workload (1KB copy vs 100bytes copy)
Short-cut approach shows best performance in uniform workload even compared with partitioned cache
17%
9%
Single node performance

## Slide 23: Which will DRAM cache approach be better?
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network
DRAM
DRAM
DRAM
DRAM
CPU
CPU
CPU
CPU
NVM
NVM
NVM
NVM
FAM
Communications and memory fabric
Network
Local APP or Server
Local APP or Server
Uniform? Zipfian?
Uniform pattern
Partitioned approach: hybrid cache will be better
Shared approach: short-cut cache will be better

## Slide 24: Summary
Memcached library that serves local and server API for our FAM-aware key-value store
Implementing short-cut pointer based caching policies in Memcached
Evaluating the performance of each cache policies
Future work (Internship end date: September 22)
  Code cleaning for Memcached library
  Evaluation performance in multi-node environment

## Slide 25: Backup

## Slide 26: Read-only (100% read)
Chart: High skew
kvs | 98.5467
Original_mc | 105.7697
full | 113.5427
short | 182.3433
hybrid | 144.2763
Chart: Low skew
kvs | 65.3437
Original_mc | 62.1512
full | 61.3631
short | 80.5862
hybrid | 64.0331
Chart: Zipfian
kvs | 114.841
Original_mc | 202.699
full | 202.7137
short | 152.5637
hybrid | 206.438

## Slide 27: Read-only (100% read)
Chart: Throughput (KTPS)
| High skew | Low skew | Zipfian
kvs | 98.5467 | 65.3437 | 114.841
hybrid-partitioned | 144.2763 | 64.0331 | 206.438
hybrid-versioned | 134.5307 | 63.6349 | 167.2237

## Slide 28: Cache hit rate of each workloads
Chart: Balanced workload
| High skew | Low skew | Zipfian
full | 67 | 8 | 94
short | 99 | 35 | 95
hybrid | 99 | 42 | 95
Chart: Read-only workload
| High skew | Low skew | Zipfian
full | 40 | 4 | 95
short | 99 | 51 | 95
hybrid | 99 | 36 | 95
Chart: Read-heavy workload
| High skew | Low skew | Zipfian
full | 70 | 10 | 94
short | 99 | 35 | 95
hybrid | 99 | 42 | 95